## Slide 1: F5 rSeries Learning with Alexander S

## Slide 2: Agenda 
  iSeries to rSeries
  F5OS Basic Setup
  F5OS Upgrade Procedure
  VLAN and LAG Configuration
    Configure VLANs
    Configure LAG (Link Aggregation Group)
    Assign VLANs to the LAG
  Tenant OS Deployment Preparation
  Tenant OS Deployment
  rSeries Tenant Basic Setup
  High Availability (HA) in rSeries Tenants
    Best Practices for rSeries Tenant HA
    rSeries Tenant HA Configuration

## Slide 3: Chapter 6 – Tenant OS deployment

## Slide 4: Chapter 6 – Tenant OS deployment This video is a continuation of Chapter 05.

## Slide 5: Chapter 6 – Tenant OS deployment F5-Host1.Lab.ae – Tenent01 deployment details
  Tenant name – prod-lb1
  Tenant type – Bigip
  Tenant image – TMOS-17.1.2.2
  Mgmt IP – 10.10.5.21/24
  Mgmt Gw – 10.10.5.1
  Vlans assignment
  Data Vlan – 230 & 231
  Ha vlan – 4001
  MAC block Size – Large
  Resource Provisioning – Go with recommended
  & Select 4vCPU
  Disk Size – Allocate 160GB
  Initial state – Configured
  Middle state – Provisioned
  End state – Deployed
  Crypto Acceleration – Enabled
  Appliance mode – Disabled

## Slide 6: Chapter 6 – Tenant OS deployment Tenent01 deployment details – Advanced mode
Advanced mode
For production environments, Advanced Mode is recommended.
This mode provides flexibility to adjust DRAM allocation based on the modules installed (such as LTM, ASM, or APM).
Recommended Mode
Such customization is not possible in Recommended Mode.

## Slide 7: Chapter 6 – Tenant OS deployment Tenant deployment details – Disk image size
  Four types of BIG-IP tenant images available for rSeries.
  Each image type has different system resource requirements and supports different sets of modules.

## Slide 8: Chapter 6 – Tenant OS deployment Tenant deployment details – Crypto Acceleration
  To offload SSL/TLS task to rSeries Crypto Accelerator hardware

## Slide 9: Chapter 5 – Tenant OS deployment Preparation 6. Understanding and Changing Tenant Deployment State
Configured
Provisioned
Deployed
Tenant’s settings and parameters are defined and saved in the F5OS
System resources such as vCPU, memory, and disk space are allocated to the tenant.
The tenant is active and running. It is utilizing the allocated CPU, memory, and virtual disk to perform its intended functions.
Settings & Parameters
CPU, DRAM and HDD assigned
CPU, DRAM and HDD assigned
System is active
Only for the initial deployment
No resources allocated
Tenant is not active!

## Slide 10: Chapter 5 – Tenant OS deployment Preparation 6. Understanding configured to provisoned
Configured
Provisioned
Tenant’s settings and parameters are defined and saved in the F5OS
System resources such as vCPU, memory, and disk space are allocated to the tenant.
Settings & Parameters
CPU, DRAM and HDD assigned
Only for the initial deployment
No resources allocated
Tenant is not active!
Provisioning

## Slide 11: Chapter 6 – Tenant OS deployment F5-Host2.Lab.ae – Tenent02 deployment details
  Tenant name – prod-lb2
  Tenant type – Bigip
  Tenant image – TMOS-17.1.2.2
  Mgmt IP – 10.10.5.31/24
  Mgmt Gw – 10.10.5.1
  Vlans assignment
  Data Vlan – 230 & 231
  Ha vlan – 4001
  MAC block Size – Large
  Resource Provisioning – Go with recommended
  & Select 4vCPU
  Disk Size – Allocate 160GB
  Initial state – Configured
  Middle state – Provisioned
  End state – Deployed
  Crypto Acceleration – Enabled
  Appliance mode – Disabled

## Slide 12: Chapter 6 – Tenant OS deployment High availability between the tenant01 & tenant02

## Slide 13: Chapter 6 – Tenant OS deployment F5-Host2.Lab.ae – Tenent02 deployment details
  Tenant name – prod-lb2
  Tenant type – Bigip
  Tenant image – TMOS-17.1.2.2
  Mgmt IP – 10.10.5.31/24
  Mgmt Gw – 10.10.5.1
  Vlans assignment
  Data Vlan – 230 & 231
  Ha vlan – 4001
  MAC block Size – Large
  Resource Provisioning – Go with recommended
  & Select 4vCPU
  Disk Size – Allocate 160GB
  Initial state – Configured
  Middle state – Provisioned
  End state – Deployed
  Crypto Acceleration – Enabled
  Appliance mode – Disabled

## Slide 14: Please continue by watching the next video. Next video is – rSeries Tenant Basic Setup – Thank you!!!
Chapter 6 – Tenant OS deployment successfully done!!!